## Slide 1
Get initial position of male and female voles
Read Serial ports and get tags on antennas 1-4
Determine what cage each animal is in (direction logic)
Read status on each door
Is door closed?
Check status of lever(s)
Is the lever pressed?
Open door
Are voles in diff cages?
Is the IR beam unobstructed?
Close door
END
END
END
Update object properties
Update object properties
Update object properties
Update object properties
Update object properties
LEGEND
Process
Function Candidate
Function used multiple times
Arduino Based Decision Tree

## Slide 2
MODE 1: Listening for lever press,
Animals in separate cages,
Door to test animal is closed
Continuous monitoring of RFID pings on a separate core. Pings update a shared queue.
MODE 2: Animal moving between cages,
Door to large cage is in transition,
State determined by RFID
SHARED DATA QUEUE OF RFID PINGS AND TAGS
Lever press moves to next mode
MODE 3: Animals are in same cage,
All doors are open,
Monitoring RFID movement
Door closes when animal has successfully moved cages
Pull RFID Data
Pull RFID Data
Exit when test animal exits large cage
Exit when animal moves to small cage

## Slide 3
Is there a lever press?
Door Opens
Track RFID
Are Animals in same cage?
Track RFID
Animal in separate cages?
Door Closes
Ping when animals get separated
Update Door Queue
Update Door Queue
Shared RFID Queue
Mode 1
Mode 2
Mode 3
YES
NO
Queue Data
Thread
Python Decision Tree

## Slide 4
Define Thread Functions
Wait for other threads to end
RFID 1
Setup Serial Port
Read Serial Port
Is there a vole that pings?
Output to Shared Queue:
RFID #,
Vole #
RFID 2
Wait for other threads to end
Setup Serial Port
Read Serial Port
Is there a vole that pings?
Output to Shared Queue:
RFID #,
Vole #
RFID 3
Wait for other threads to end
Setup Serial Port
Read Serial Port
Is there a vole that pings?
Output to Shared Queue:
RFID #,
Vole #
RFID 4
Wait for other threads to end
Setup Serial Port
Read Serial Port
Is there a vole that pings?
Output to Shared Queue:
RFID #,
Vole #
RFID Tracking Decision Tree
Individual Thread

## Slide 5
Initialize voleTags Queue
Output vole number and rfid tag
Output “none”
Output vole number and rfid tag
Output “none”
Start Thread 1
Read sensor signal
Did it ping vole 1?
Did it ping vole 2?
Set event to FALSE
Set event to TRUE
WAIT for Main Event
Start Thread 2
Read sensor signal
Did it ping vole 1?
Did it ping vole 2?
Set event to FALSE
Set event to TRUE
WAIT for Main Event
Start Schedule Thread
Set Main Event to FASLE
WAIT for thread1 event
WAIT for thread2 event
Set Main Event to TRUE
NOTE: The threads in blue are the threads assigned to each rfid chip. This is not limited to only two threads, copy the thread for as many rfid chips as you have. The process is the same for each, simply add an eventX.wait() command in the scheduling thread (purple) after the other wait() commands. This is meant to be a scalable architecture.
RFID Threading Flow Chart

## Slide 6
2
Cage Numbering System

## Slide 7: Old Slides

## Slide 9
Initialize voleTags Queue
Initialize time synchronization queue
Start Thread 1
Read sensor signal
Did it ping vole 1?
Output vole number and rfid tag
Output “none”
Did it ping vole 2?
Output vole number and rfid tag
Output “none”
Read time queue
Number < # of threads?
Add 1 to indicate finished sensing
Output 0
END
Read time queue
Start Thread 1
Read sensor signal
Did it ping vole 1?
Did it ping vole 2?
Read time queue
Number < # of threads?
Read time queue
END