## Slide 1
Get initial position of male and female voles
Read Serial ports and get tags on antennas 1-4
Determine what cage each animal is in (direction logic)
Read status on each door
Is door closed?
Check status of lever(s)
Is the lever pressed?
Open door
Are voles in diff cages?
Is the IR beam unobstructed?
Close door
END
END
END
Update object properties
Update object properties
Update object properties
Update object properties
Update object properties
LEGEND
Process
Function Candidate
Function used multiple times
Arduino Based Decision Tree

## Slide 2
MODE 1: Listening for lever press,
Animals in separate cages,
Door to test animal is closed
Continuous monitoring of RFID pings on a separate core. Pings update a shared queue.
MODE 2: Animal moving between cages,
Door to large cage is in transition,
State determined by RFID
SHARED DATA QUEUE OF RFID PINGS AND TAGS
Lever press moves to next mode
MODE 3: Animals are in same cage,
All doors are open,
Monitoring RFID movement
Door closes when animal has successfully moved cages
Pull RFID Data
Pull RFID Data
Exit when test animal exits large cage
Exit when animal moves to small cage

## Slide 3
Is there a lever press?
Door Opens
Track RFID
Are Animals in same cage?
Track RFID
Animal in separate cages?
Door Closes
Ping when animals get separated
Update Door Queue
Update Door Queue
Shared RFID Queue
Mode 1
Mode 2
Mode 3
YES
NO
Queue Data
Thread
Python Decision Tree